## Slide 1: Gateway Basic and OTA
2019

## Slide 2: Agenda
Hands-on : Control Zigbee Devices with MQTT Clients
Hands-on : OTA
Q & A

## Slide 3: Gateway Overview
Zigbee Gateway
MQTT/CoAP
Zigbee
Zigbee Gateway translate Zigbee messages and MQTT messages from each other.

## Slide 4: MQTT
  Publish/Subscribe
  Topic
    Represents a message type
    Also include the address info
  Payload
    Message content. (xml or JSON)
Notes: Broker

## Slide 5: MQTT Hands-on
Z3Gateway
Network
MAC
PHY
EFR32
Zigbee Application
Host
MQTT
Client
UART/SPI
MQTT
Broker
Light
Zigbee
Mosquitto Broker
MQTT Client
MQTTBox
Z3LightSoc.s37
bootloader-storage-internal-single-combined-Z3light.s37
Z3GatewayHost.exe
ncp.s37
bootloader-xmodem-uart.s37

## Slide 6: Hands-on: Install MQTT Broker --- Mosquitto
mosquitto-1.6.7-install-windows-x64.exe
Make sure the service “Mosquitto Broker” is running
  “win+R” then input “services.msc” to start the service manager, then check the service state
  If it’s not running, right click and select “start”

## Slide 7: Hands-on: MQTT Client

## Slide 8: Hands-on: MQTT Client

## Slide 9: OTA Overview
Z3Gateway
Network
MAC
PHY
EFR32
Zigbee Application
Host
MQTT
Client
UART/SPI
OTA Client
Z3GatewayHost.exe
New image
ncp.s37
bootloader-xmodem-uart.s37
V200
Build/exe/ota-files/Client.ota
SPI Flash
V100 Client.s37
bootloader-storage-spiflash-single.s37
New image file will be transferred from server to client.
Client will split the GBL file out and save it to storage.

## Slide 10: OTA Procedure
OTA Server
OTA Client
Query Next Image Request
Find OTA file according to
Hardware version
Image type
Manufacture ID
Firmware version
Query Next Image Response
Image Block Request
Image Block Response
Image Block Request
Image Block Response
……
Upgrade End Request
Upgrade End Response
Erase the storage and prepare to receive new image
Save received data
Check if received image is valid
Reset and bootload the new image

## Slide 11: Commands
Show OTA images on server
Show version on client

## Slide 12: Q&A
Q&A

## Slide 13: Thank you!
Notes: Thanks