## Slide 1: IoT OTA Update Project Proposal
Mark Ding | March 11, 2020

## Slide 2: Agenda
OTA Introduction
Bluetooth OTA
Zigbee OTA
Proprietary OTA
Z-Wave OTA
Proposal on Improvement of OTA Update

## Slide 3: OTA Introduction
OTA (over-the-air) is a mechanism for remotely updating IoT device with new settings or firmware
The OTA Update mechanism is a core part of a IoT system’s architecture
OTA architectures for IoT
  It contains two major part: Client and Server.
    Client: It can be the IoT end device or gateway which is capable of receiving new firmware image from a remote server.
    Server: It is responsible for sending firmware image to the client. It can be cloud or local host that is able to locally connect with client device.
Existing Implementation
  Server:
    Host app runs on laptop, connects with a wireless device via UART/SPI.
    Sending firmware image through the wireless device to the client device.
  Client:
    Wireless client device join the network or directly communicate with server to receive the firmware image over-the-air.
We would like to introduce more in details for various wireless product at following sections

## Slide 4: Bluetooth OTA
Client – (GATT Server in Bluetooth)
  WSTK running in SoC mode
  Application Bootloader + AppLoader
  External or internal flash as image storage space
  Run batch file to create bootloader files
Server – (GATT Client in Bluetooth)
  WSTK running in NCP mode
    Standalone DFU Bootloader
  ota_dfu App running on Windows with Cygwin.
  Communicating between NCP device and PC host via BGAPI
OTA Update
  The mesh OTA update is not defined by SIG
  Run ota-dfu from host along with client device mac address
  It takes 33 seconds to finished the update

## Slide 5: Zigbee OTA
Client
  WSTK running in SoC mode
  Application Bootloader
  External or internal flash as image storage space
  Require software configuration to enable OTA related plugin
Server
  WSTK running in NCP mode
    Standalone xmodem Bootloader
  Z3Gateway host App running on Windows with Cygwin
  Communicating between NCP device and PC host via EZSP
OTA Update
  Server form the network by command line input
  Client join the network by command line input
  Start the OTA progress by command line at client
  It takes 5.5 minutes to finish the update

## Slide 6: Proprietary OTA
Client
  WSTK running in SoC mode - Sensor
  Application Bootloader
  Require software configuration to enable OTA related plugin
Server
  WSTK running in SoC mode - Sink
    Application Bootloader
  Require software configuration to enable OTA related plugin
  External or internal flash as image storage space
OTA Update
  Program image file to server WSTK by commander tool.
  Server form the network by command line input
  Client join the network by command line input
  Start the OTA progress by command line at server side

## Slide 7: Z-Wave OTA
Client – (Slave in Z-Wave)
  WSTK running Soc mode - SwitchOnOff
  Application OTA Bootloader in hex file format
  Flash Bootloader sample keys by commander tool
Server – (Controller in Z-Wave)
  PC Controller GUI tool running on Windows
  Need a UZB7 USB dongle attached to PC
  Communicating between UZB7 and PC Controller via Serial API
OTA Update
  Server forms the network by click button on the GUI tool
  Client start joining the network by pressing a button
  Server accept the request with Client SN input
  Server start the OTA progress
  It takes 10+ minutes to finish the update
UZB7
Slave
Host PC Running Controller GUI Tool

## Slide 8: New IoT OTA Design Hardware Diagram
Host PC running application
WSTK in NCP Mode
Wireless Protocol
Serial UART
WSTK in SOC Mode
OTA Client
OTA Server

## Slide 9: Proposal on Improvement of OTA Update
  Bootloader
    Both client Soc and server NCP WSTK use Gecko application bootloader.
  NCP
    We choose NCP at server side since it is popular design on Gateway and easy to maintain.
  Host
    Every host app can be built under Cygwin. Unique compiling environment
  Script
    Using Python 3.x to manage the whole OTA update progress at host side.
    It can keep current host app without much changes to work with Python.
    Make a xml or JSON as unique configuration file for various wireless protocol OTA update.
  Network
    Form and join network automatically, no need command line interaction.
  Pro
    We take advantage of each wireless product to make the OTA update better than before.
    We make the unique way of OTA update across the products.
    Simplify the OTA procedure and improve developer experience.
  Con
    It is a very time cost project as it makes a big changes across the various products.

## Slide 10
Thank You