## Slide 1: EmberZnet and WSTK
2019

## Slide 2: Agenda
Overview
Wireless Gecko Socs
EmberZnet SDK & Software
Development Tools

## Slide 3: Zigbee Portfolio
Development Tools
Software + Stacks
SoCs + Modules
Notes: Silicon Labs provides IoT solutions that include hardware, software and tools.
Lets take a look at the Wireless Gecko series Socs first

## Slide 4: Wireless Gecko Socs
 | Mighty Gecko 256 to 1024 kB 40+ Parts | 2.4 GHz | 2.4 GHz | 2.4 GHz | 2.4 GHz Sub-GHz
 | Blue Gecko 128 to 1024 kB 50+ Parts |  |  | 2.4 GHz | 2.4 GHz Sub-GHz
 | Flex Gecko 32 to 1024 kB 40+ Parts |  |  |  | 2.4 GHz Sub-GHz
Notes: As you can see from this slide there are 3 different families in the Wireless Gecko portfolio that support different wireless standards.
Mighty Gecko is the superset part. While it is focused on 2.4 GHz mesh, including zigbee and Thread, it supports Bluetooth Low Energy and can support both 2.4 GHz and sub-GHZ for proprietary applications. This makes it a great option for customers that want a single design to support multiple options or want the capability for a single product in the field to support multiple protocols. With 256K to 1meg of Flash and over 40 parts, including SoCs and modules, it is the ideal multi-protocol solution.

## Slide 5: Mighty Gecko SoC Comparison
 |  | EFR32MG1 | MG12 | MG13 | MG21-New
Protocols |  |  | + BT 5 (2 Mbps) | + BT 5 (2 Mbps & Long Range) | + BT 5 (2 Mbps)
Freq. Bands |  | 2.4GHz + Sub-GHz | → | → | →
Core |  | Cortex-M4 (40 MHz) | → | → | Cortex-M33 (80 MHz)
Max Flash |  | 256 kB | 1 MB | 512 kB | 1 MB
Max RAM |  | 32 kB | 256 kB | 64 kB | 96 kB
Security |  | AES-128/-256, ECC, SHA-1/-2 | + TRNG | → | + TRNG TrustZone
TX Power |  | +19 dBm | → | → | →
802.15.4 Sensitivity |  | -99 dBm | -102.7 dBm | → | -104 dBm
Active Current |  | ~60 µA/MHz | → | → | ~50.9 µA/MHz
Sleep Current |  | 2.5 µA | 1.5 μA | → | 4.5 μA
TX Current @ +0 dBm |  | 8.2 mA | 8.5 mA | → | 9.3 mA
RX Current (BLE) |  | 8.7 mA | 10.0 mA | → | 8.8 mA
Operating Voltage |  | +1.85 - 3.8V | +1.8 – 3.8V | → | +1.71 – 3.8V
Max GPIO |  | 31 | 65 | 31 | 20
Other |  | IDAC | VDAC, LESENSE, OPAMP, Cap Sense | VDAC, LESENSE, OPAMP, Cap Sense, PLFRCO | 
Notes: Now let’s take a look at the Mighty gecko series products.
MG12/MG13/MG14 are almost the same except the flash size and ram size.
MG14 is pin compatible with MG1 series. They are mainly used on NCP. Because the flash size is small.

## Slide 6: EFR32MG12 Wireless Gecko
32-bit bus
Peripheral Reflex System
Energy Management | 
Voltage Regulator | Voltage Monitor
DC-DC Converter | Brown-out Detector
Power-on Reset | 
Clock Management | 
High Freq Crystal Osc | High Freq RC Osc
Auxiliary RC Osc | Ultra Low Freq RC Osc
Low Freq Crystal Osc | Low Freq RC Osc
Analog Modules | 
ADC | 2x Analog Comparators
IDAC | 
VDAC & OPAMP | Cap Sense
Security
Crypto AES, ECC, SHA
CRC32
TRNG
CPU and Memory |  | 
ARM Cortex-M4 w/ FPU + MPU | 1 MB Flash | ETM
Debug Interface | 256 kB RAM | LDMA Controller
Serial Interfaces | 
4x USART | Low Energy UART
2x I2C | 
Timers and Triggers | 
4x Timer/ Counter | Low Energy Timer
LESENSE | Watchdog
Pulse Counter | Protocol Timer
RTC | Cryotimer
Radio | 
2.4 GHz (int. balun) | Sub-GHz
Integrated PA | Radio Controller
Packet Trace | Radio Crypto
EM4H
Hibernate
EM1
Sleep
EM0
Run
EM2
Deep Sleep
EM3
Stop
EM4S
Shutoff
Feature available down to Energy Mode
I/O Ports | 
External Interrupt | Up to 65 GPIO (5V Tol)
Pin Reset | GPIO Wakeup
Notes: As you can see from the block diagram, Mighty Gecko is a full featured MCU and wireless SoC.
The part shown is the EFR32MG12 that was launched in March of 2017, but there are other products in the portfolio that provide developers with the exact features set they need.
The MCU is based on Gecko technology so not only does it provide a rich set of peripherals, but also offers exceptional low power capabilities. Low power is more then just low active and sleep states. It is about how the entire system operates in these modes and how quickly it can switch between them. The shaded blocks show what operating modes the feature can operate in. You will notice that a significant amount of blocks can work in the deeper sleep modes, which dramatically reduces power consumption of the system. Features like LESENSE and PRS allow for autonomous operating of peripherals, lowering system power consumption.
With up to 1024k of Flash and 256k of RAM developers have the memory to support not only multi-protocols, but also complex applications. Advanced energy management provides for voltage support for from 1.8 to 3.8 volts and the DCDC ensure low active and sleep currents.
Serial I/O includes up to 4 USARTs, 2 I2C and even a low energy UART that is supported all the way down to deep sleep. The device can support both 16-bit and 32-bit timers with up to 3 PWM per timers.
Features like LESENSE and Pulse counters are ideal for flow meters while the integrated cap sense provides a great option for removing mechanical switches from applications.
The radio has options for both 2.4 GHz and sub-GHz with output power up to +20 dBm and excellent sensitivity eliminates the need for costly front end modules.
And of course, no system is complete without the necessary security blocks to offload the cryptos required for IoT devices.
Wireless Gecko brings together all the critical components for the ultimate IoT hardware platform.

## Slide 7: Software and Stack
Development Tools
Software + Stack
SoCs + Modules
Notes: Now let talk about Zigbee software and stack.
Architecture
Soc & NCP
Bootloader
Token
Event

## Slide 8: Silicon Labs Zigbee Options
Medium Access
Physical RF
Device Discovery
Network Organization
Message Relay
Route Discovery
Security
Determine Device Relationships
Manage Network
Initiate and Join Network
Send and Receive Messages
Zigbee Pro Feature Set
System-on-Chip (SoC)
  - IEEE 802.15.4 compliant radio
  - Integrated microcontroller
  - Integrated peripherals (ADC, encryption engine, GPIO, etc.)
  - Lowest system cost
Network Co-Processor
SoC
Application Profiles
(defined by Zigbee and OEMs)
Zigbee
(defined by Zigbee Alliance)
Radios
(defined by IEEE 802.15.4)
Host
NCP
  - Self-contained Zigbee Stack
  - Dedicated function device
EZSP
Notes: Silicon Labs provides two models for Zigbee design: the SoC model, and the NCP model.
In the SoC model, all stack layers as well as the application are implemented on a single chip, with lower level stack functions implemented in hardware as peripherals of the microcontroller.
Access to the stack functionality here is generally provided as library API calls.
In NCP model, the stack and low-level radio functionality all reside on one chip for best integration and efficiency where the stack features are concerned.
However, the application interface to the stack is through a serial interface such as SPI or UART, rather than a library of function calls.
The host and NCP uses a proprietary serial protocol to exchange data. The protocol is named EZSP, which is short for EmberZnet serial protocol.
This model allows for great flexibility on the application design and the host processor architecture. It allows the application designer to ignore many implementation details about the stack itself. You may

## Slide 9: Bootloader
Type | 
Bootloader-xmodem-uart | Also called standalone bootloader. Mainly used on NCP.
Internal Storage Bootloader | Used on Soc. Store new image in internal flash.
External Storage Bootloader | Used on Soc. Store new image in SPI flash.
Type | Pre-built
Bootloader-xmodem-uart | v2.6\platform\bootloader\sample-apps\bootloader-uart-xmodem
Internal Storage Bootloader | v2.6\platform\bootloader\sample-apps\bootloader-storage-internal-single
External Storage Bootloader | v2.6\platform\bootloader\sample-apps\bootloader-storage-spiflash-single

## Slide 10: EmberZnet SDK
Resources | 
v2.6\protocol\zigbee\documentation | 
v2.6\protocol\zigbee\app\framework\plugin | 
v2.6\protocol\zigbee\app\framework\plugin-host | 
v2.6\protocol\zigbee\app\framework\plugin-soc | 

## Slide 11: Development Tools
Development Tools
Software + Stack
SoCs + Modules
Notes: Now I will introduce our develop tools.

## Slide 12: Wireless Starter Kit
+
Wireless Starter Kit
Swappable Radio Boards
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 13: Tools
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 14: Create a Zigbee Project – 1/2
“File””New””Project”
Choose “Zigbee” Application
Choose “SoC” Architecture
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 15: Create a Zigbee Project – 2/2
Choose example or start from minimal
Name project
Choose “Board”/”Part” and toolchain
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 16: AppBuilder - General
Initial project files
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 17: AppBuilder - Stack
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 18: AppBuilder – Cluster Attributes
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 19: AppBuilder – Cluster Commands
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 20: AppBuilder - Plugins

## Slide 21: Typical Plugins
Coordinator
  Security Core Library
  NVM3
  Simple Main
  Zigbee Pro Stack Library
  Network Creator
  Network Creator Security
Router
  Security Core Library
  NVM3
  Simple Main
  Zigbee Pro Stack Library
  Network Steering
  Update TC Link Key
End Device
  Security Core Library
  NVM3
  Simple Main
  Zigbee Pro Leaf Library
  Network Steering
  Update TC Link Key
  End Device Support
  Idle/Sleep

## Slide 22: AppBuilder - Callbacks
Notes: Silicon Labs has a great development platform based on the Wireless STK and radio boards. The Wireless STK provides the starting point for development providing the hardware and access to mesh software.
Different radio boards for both SoCs and modules plug into the WSTK main boards, providing a unified development platform from both the hardware and software perspective.

## Slide 23: Callbacks Flow

## Slide 24: AppBuilder – Custom settings

## Slide 25: Generated Files
File | Description
<projectname>.h | main header file, plugin settings
<projectname>_callbacks.c | Customer implementation
<projectname>_endpoint_config.h | defines the endpoints and attributes
znet-cli.c | CLI command list
client-command-macro.h | macros which will be used in filling messages
call-command-handler.c | Cluster command process
attribute-id.h/attribute-size.h/attribute-type.h/att-storage.h | Attribute related
af-structs.h | Data structs
af-gen-event.h | Event/handler pair
Notes: Show the generated files.

## Slide 26: Hardware Configurator
Notes: Show the generated files.

## Slide 27: Flash/Program
Method 1:
Method 2:

## Slide 28: CLI Commands
plugin network-creator form [useCentralizedSecurity:1] [panId:2] [radioTxPower:1] [channel:1]
  Form a network with specified parameters.
    useCentralizedSecurity - BOOLEAN - Whether or not to form a centralized network. If this value is false, the device will attempt to join a distributed network.
    panId - INT16U - PanID of the network to be formed
    radioTxPower - INT8S - Tx power of the network to be formed
    channel - INT8U - channel of the network to be formed
plugin network-creator-security open-network
  Open the network for joining.
plugin network-creator-security open-with-key [eui64:8] [joiningLinkKey:-1]
  Open the network that would only allow the node with specified EUI and link key pair to join.
    eui64 - IEEE_ADDRESS - The EUI64 of the joining device.
    joiningLinkKey - OCTET_STRING - The link key that the joining device will use to enter the network.

## Slide 29: CLI Commands
plugin network-steering start [options:1]
  Starts the network steering process.
    options - INT8U - A mask of options for indicating specific behavior within the network-steering process.
zcl on-off toggle
send [id:2] [src-endpoint:1] [dst-endpoint:1]
  Send a pre-buffered message from a given endpoint to an endpoint on a device with a given short address.
    id - INT16U - short id of the device to send the message to
    src-endpoint - INT8U - The endpoint to send the message from
    dst-endpoint - INT8U - The endpoint to send the message to

## Slide 30: Debug
emberAfCorePrint(…) - prints a single line without a carriage return
emberAfCorePrintln(…) - prints a single line with a carriage return
emberAfCorePrintBuffer( buffer, len, withspace ) – prints a given buffer as a series of hex values
emberAfCorePrintString( buffer ) – prints a given buffer as a string of characters

## Slide 31: Network Analyzer
Start Capture

## Slide 32: Thank you!